| MODEL | KPC-S20CP4, KPC-S20P1, KPC-S20B |
| --- | --- |
| Signal Format | NTSC | PAL |
| Image Device | SONY 1/4" SUPER HAD COLOR CCD |
| Scanning System | 2 : 1 Interlace |
| Scanning Frequency | H : 15.734 (KHz), V : 59.94 (Hz) | H : 15.635 (KHz), V : 50 (Hz) |
| Total Pixels | 537(H) x 505(V) | 537(H) x 597(V) |
| Effective Pixels | 510(H) x 492(V) | 500(H) x 582(V) |
| Horizontal Resolution | More than 380 TV Lines |
| Electronic Shutter | 1/60 - 1/100,000sec Auto | 1/50 - 1/100,000sec Auto |
| S/N Ratio | More than 46dB (AGC OFF) |
| Signal Process | Digital Signal Processor |
| White Balance | Automatic (2,400˚ K ~ 8,000˚ K) |
| Sensitivity | 0.5 Lux / F 1.2, 1.0 Lux / F2.0 (AGC ON) |
| Gamma Correction | Γ= 0.45 |
| Sync System | Internal |
| Video Output | Composite 1 [Vp-p] 75(Ω) unbalanced |
| Power Supply | DC 12V (±10%) |
| Operating Temperature | -10˚ C ~ + 50˚ C |
| Storage Temperature | -20˚ C ~ + 60˚ C |
| Operating Humidity | 10% ~ 80% |
| Lens | f 4.3mm Super Cone Pinhole Lens |